## Slide 1
SPACE-GRADE
MECHANICAL FAULT DETECTOR
Radiation-Hardened Vibration Analysis ASIC
Team B22 — Space Jam SSCS Chipathon 2026 Target: GF180MCU (180nm CMOS)
Spacecraft Mechanical Failures
Structural degradation generates distinct vibration signatures BEFORE catastrophic failure occurs. Edge detection is vital.
🔧 Reaction Wheel Bearings → 1 - 2 kHz range (indicator of bearing wear)
⚙️ Cryogenic Pumps → 3 - 5 kHz range (indicator of pump fatigue)
📡 Deployment Hinges/Gears → 8 - 12 kHz range (indicator of structural stress/damage)
The Edge Processing Challenge: Streaming raw vibration data continuously to the host computer consumes excessive bandwidth and power. Our ASIC performs real-time onboard Goertzel spectral filtering and flags fault alerts directly at the sensor node, fitting within a strict 600×600 µm silicon footprint.
Notes: Hello, I am presenting Team B22's Space-Grade Mechanical Fault Detector. Critical satellite components, such as reaction wheels and cryogenic pumps, experience mechanical degradation that generates distinct, high-frequency vibration signatures long before catastrophic failure occurs.
Streaming raw high-speed vibration data continuously to the central spacecraft computer consumes excessive power and telemetry bandwidth. Our solution is a dedicated, radiation-hardened edge-processing ASIC that performs Goertzel-based spectral analysis directly at the sensor node and raises a hardware interrupt only when an anomaly is verified, respecting a strict 600-by-600 micron area limit.

## Slide 2
SPACE-GRADE MECHANICAL FAULT DETECTOR
ASIC System Architecture & Dataflow Pipeline
Modular Pipeline Design
1. SPI Master: Configures and reads 48-bit XYZ samples from IIS3DWB MEMS sensor.
2. SPI-APB Interface: Buffers samples and decouples timing between SPI and APB clocks.
3. TMR Register Bank: Radiation-hardened configuration storage (coefficients, thresholds).
4. Axis Sequencer: Time-multiplexes X, Y, Z axis data to process them sequentially.
5. Goertzel Core: Custom hardware DSP engine for targeted frequency bin filtering.
6. Magnitude Compute: Converts recursive filter states into usable spectral energy.
7. Fault Flagger: Compares spectral magnitude to thresholds and asserts interrupt.
8. APB Master: Interfaces with system bus for register reads and configuration.
✨ Innovation: Direct Digital MEMS Interface Eliminates analog radiation-vulnerable ADCs on-chip. Operates end-to-end digitally using the space-proven IIS3DWB digital output.
Notes: This slide shows the modular hardware pipeline. Our system comprises eight custom modules. First, the SPI Master interfaces directly with the MEMS accelerometer, automatically configuring it on boot and reading 48-bit XYZ samples. The samples are buffered by the SPI-APB interface.
To save critical die area, instead of implementing three parallel DSP pipelines, the Axis Sequencer time-multiplexes a single Goertzel engine sequentially across the X, Y, and Z axes. The resulting states are passed to the Magnitude Compute and Fault Flagger, which assert interrupts if thresholds are breached. By interfacing directly with a digital sensor, we avoid vulnerable on-chip analog circuits.

## Slide 3
SPACE-GRADE MECHANICAL FAULT DETECTOR
Direct Digital Sensor Interface (SPI & APB Master)
SPI Master Interface (Module 1)
• Protocol: SPI Mode-3 (CPOL=1, CPHA=1)
• Acquisition: 48-bit XYZ burst reads minimize overhead
• Clock Domain Crossing: 2FF synchronizers prevent metastability between domains
• Triggering: Event-driven by sensor DRDY interrupt
• Shared FSM: Seamlessly handles boot configuration (writing 4 registers) and runtime acquisition
APB Master & Bus Interface (Modules 2 & 3)
• Protocol: Standard AMBA APB protocol
• Interface: Converts internal SPI sample updates into APB transactions
• FSM Control: Lightweight 3-state control (IDLE, SETUP, ACCESS)
• Wait States: Full PREADY support allows slow peripherals
• Efficiency: Request-driven transactions minimize switching activity, conserving dynamic power
• decoupling: Decouples fast SPI clock domain from system APB bus clock domain
Notes: Here we look at the communication interfaces. The SPI Master communicates with the sensor using SPI Mode 3, executing 48-bit burst reads of XYZ acceleration data. Because the sensor operates on an independent clock, we route inputs through double flip-flop synchronizers to avoid clock domain crossing issues.
On the right, we have the SPI-APB interface and the APB Master. The SPI-APB wrapper stores the latest sensor sample, and the APB Master uses a simple 3-state FSM to issue transactions. It includes PREADY support to allow wait states when interfacing with slower system registers, and uses request-driven clocking to keep power consumption to a minimum.

## Slide 4
SPACE-GRADE MECHANICAL FAULT DETECTOR
Hardware-Optimized DSP Engine (Goertzel Core)
The Goertzel Algorithm
Recurrence Relation (Second-Order IIR Filter): v[n] = x[n] + C · v[n-1] - v[n-2]
Why Goertzel over FFT? Instead of computing the entire frequency spectrum, the Goertzel algorithm computes energy at specifically targeted bins. This drastically reduces mathematical complexity, silicon area, and power consumption, making it ideal for edge processing.
• Bins monitored: 3 programmable bins (1k, 5k, 10k Hz) • Execution speed: 6 clock cycles per sample • Control: Triplicated (TMR) state transition logic
DSP Hardware Features (Module 6)
• Shared Multiplier: A single multiplier block is shared across all three frequency bins via time-multiplexing, avoiding logic duplication.
• Saturating Q8.15 Fixed-Point: Handles fractional math and prevents arithmetic overflow corruption in recursive loops.
• Operand Isolation: Input registers to the multiplier are gated (isolated) when the core is idle.
• Power Savings: With the multiplier active only 6 cycles out of every 1875 cycles (sample period), the DSP engine is idle 98.4% of the time, dramatically reducing dynamic power.
Notes: The Goertzel Core is the DSP engine. Rather than calculating a resource-intensive FFT, we use the Goertzel algorithm to compute energy at three targeted frequency bins. The core executes a second-order recurrence equation using saturating Q8.15 fixed-point arithmetic.
To minimize area, all three frequency bins share a single hardware multiplier. Because the sensor's sample rate is 26.667 kilohertz and our clock is in the megahertz range, the Goertzel core only needs 6 clock cycles to process each sample. By implementing operand isolation to gate the multiplier inputs during the remaining idle cycles, the core is effectively idle 98.4% of the time, which minimizes dynamic power.

## Slide 5
SPACE-GRADE MECHANICAL FAULT DETECTOR
Magnitude Compute Engine
Goertzel Magnitude Squared
Magnitude² = v1² + v2² - C · v1 · v2
Where v1 = v[N-1] and v2 = v[N-2] represent the final states of the Goertzel core at the block boundary. The resulting magnitude represents the spectral energy at the monitored frequency.
✨ Snapshot Architecture (Module 7): At the block boundary, the Magnitude Compute module immediately captures v1, v2, the coefficient, and the axis index in snapshot registers. This allows the Goertzel Core to clear its accumulators and start filtering the next sample block immediately without stalling.
Resource Sharing (Zero-Area Multiplier)
• Shared Hardware Multiplier: The Magnitude Engine does not contain its own multiplier. Instead, it multiplexes and reuses the multiplier in the Goertzel Core, saving significant silicon area.
• Sequential Magnitude FSM: One FSM calculates the magnitude of the 3 bins sequentially (taking 8 cycles per bin, 24 cycles total). No dedicated per-bin arithmetic is duplicated.
• Triggering: The Magnitude Compute FSM remains completely idle, drawing near-zero dynamic power, until triggered at a block boundary.
• Axis Attribution: The physical axis index is snapshotted alongside Goertzel states. This guarantees that every magnitude output is correctly paired with the X, Y, or Z axis, even if the sequencer advances to another axis.
Notes: The Magnitude Compute module converts internal recursive filter states into spectral energy using the Goertzel magnitude squared equation. Because this equation requires three multiplications, we would normally need more multipliers, which are very area-expensive. Instead, our design shares the existing multiplier inside the Goertzel Core.
At the block boundary, we capture the final states in snapshot registers, freeing up the Goertzel Core to immediately start processing the next block. The Magnitude FSM then runs sequentially, reusing the shared multiplier over 24 clock cycles to compute energy for all three bins. This snapshot architecture prevents stalls and guarantees correct axis attribution.

## Slide 6
SPACE-GRADE MECHANICAL FAULT DETECTOR
Radiation Hardening by Design (RHBD) Strategy
Reliability in Space Environments
Space radiation causes Single Event Upsets (SEUs), where high-energy particles randomly flip bits in flip-flops. We implement a multi-layered defense to achieve a highly reliable ASIC.
✔ Triple Modular Redundancy (TMR): Critical configuration registers (thresholds, Goertzel coefficients), FSM state registers, and the Axis Sequencer index are triplicated.
✔ Majority Voting: In-line voters continuously resolve the three copies. Any single-bit flip is masked in a single clock cycle without interrupting operations.
✔ Background Scrubbing (Module 4): A dedicated periodic scrubber continuously checks register copies in the background and rewrites corrupted bits, preventing error accumulation.
SRAM-Free & Physical Layout Hardening
• SRAM-Free Architecture: Standard SRAM cells are highly sensitive to radiation. By storing all system configurations and DSP states in triplicated flip-flops, we eliminate memory-upset vulnerabilities.
• Substrate Taps & Guard Rings: Layout is constrained with dense substrate taps and physical guard rings surrounding active wells. This prevents Single Event Latch-up (SEL) conditions.
• Interleaved Routing: Critical redundant signals are physically separated during routing to prevent a single particle strike from corrupting multiple copies (Common Cause Failure).
Notes: Operating in orbits like LEO exposes electronics to space radiation, leading to Single Event Upsets and Latch-ups. We implement a multi-layered Radiation Hardening by Design strategy. Redundant registers are triplicated and majority voted, masking single bit flips instantly.
To prevent multiple faults from building up, a periodic background scrubber checks configuration replicas and rewrites corrupted copies. On the physical layout side, we use an SRAM-free design, dedicated guard rings, and dense substrate taps to avoid latch-ups, along with interleaved signal routing to mitigate multi-node charge collection.

## Slide 7
SPACE-GRADE MECHANICAL FAULT DETECTOR
Critical Area Constraint & Trade-off Options
The Engineering Challenge: Multi-Axis vs. Area
The IIS3DWB sensor outputs all three axes (X, Y, Z) simultaneously. However, the Chipathon die area is strictly capped at 600×600 µm. We evaluated three architectural solutions to balance area, speed, and reliability:
Option | Approach | Area Impact | Latency (3-Axis) | Status / Verdict
Option 1 | Parallel 3-Axis DSP Cores | +300 FFs (triplicated) | 19.2 ms | ❌ Exceeds 600×600 µm die limit
Option 2 | Raw Sample Buffer (512×48-bit) | +3,072 FFs | 57.6 ms | ❌ Violates SRAM-Free/RHBD rules
Option 3 | Reduced BLOCK_SIZE (512 → 171) | -3 FFs (Net Savings) | 19.2 ms | ✅ SELECTED OPTIMIZATION
Selected Optimization: Option 3 (BLOCK_SIZE = 171) By reducing the block size, we achieve a three-fold latency improvement, save register logic (reducing the block counter from 9 to 8 bits), and fit comfortably within the 600×600 µm layout constraint with zero area overhead.
Notes: This slide presents the core engineering decision of our Chipathon design. The sensor outputs all 3 axes simultaneously, but our die area budget is strictly capped at 600-by-600 microns. We evaluated three options to resolve this.
Option 1 used parallel cores but was too large. Option 2 used a sample buffer, which violated our SRAM-free radiation-hardening rules. We chose Option 3: reducing the block size from 512 to 171 samples. This not only fits within the area constraint, but actually provides a minor area reduction by saving counter bits, while improving vibration detection latency.

## Slide 8
SPACE-GRADE MECHANICAL FAULT DETECTOR
Option 3 Implementation & Trade-off Analysis
Quantitative Performance Trade-offs
Threshold Scaling Justification: Goertzel magnitude scales as N². Thus, changing BLOCK_SIZE from 512 to 171 requires scaling the detection threshold by (171/512)² ≈ 0.112. The testbench threshold was recalibrated from 120 to 14, maintaining mathematical consistency.
Parameter | Size 512 | Size 171 | Impact
Per-Axis Latency | 19.2 ms | 6.4 ms | 3× Faster Detection
Full 3-Axis Latency | 57.6 ms | 19.2 ms | 3× Faster Rotation
Bin Resolution | 52.1 Hz | 156.9 Hz | Coarser Bins (Accepted)
Threshold Config | 120 | 14 | Scaled by N² factor
Accepted Limitations & Justification
1. Sequential Processing Data Loss: Processing axes sequentially means 2 out of 3 axes are discarded during a block's acquisition window (66.7% data loss per sample).
2. Intermittent Fault Coverage: Because the DSP engine rotates X → Y → Z, it cannot detect simultaneous multi-axis faults occurring inside the same 6.4 ms window.
3. Justification for Spacecraft Applications: Mechanical failures (bearing wear, pump fatigue) degrade slowly over hours or days, not milliseconds. A 19.2 ms full-axis rotation time is orders of magnitude faster than physical fault progression. Option 3 is highly sufficient for the target application.
Notes: Reducing the block size to 171 samples results in quantitative trade-offs. On the positive side, our detection speed improves by three times, and full 3-axis rotation latency falls to 19.2 milliseconds. To maintain mathematical consistency, we recalibrated the detection threshold from 120 to 14.
On the right, we acknowledge the limitations of this choice: sequential axis processing leads to a 66.7% loss of sample data, and we cannot detect simultaneous multi-axis faults within a single window. However, because spacecraft mechanical degradation occurs slowly over hours or days, a 19.2 ms full-axis cycle is extremely fast and more than sufficient.

## Slide 9
SPACE-GRADE MECHANICAL FAULT DETECTOR
Comprehensive Verification & Regression Testing
100% Assertion Success — All 79 Verification Checks Passed
RTL updates were validated using three automated testbench environments, confirming timing closure and math precision:
Top Integration (tb_top.v) Result: 7 / 7 Passed ✅
• Case 1: Quiet normal operation (no false positives)
• Case 2: X-axis fault detected and flagged (axis reported == 0)
• Case 3: Y-axis fault detected and flagged (axis reported == 1)
• Case 4: Z-axis fault detected and flagged (axis reported == 2)
• Timing: Confirmed 6.4 ms per-axis rotation intervals
Goertzel Core (tb_goertzel_core.v) Result: All Passed ✅
• Verified second-order recurrence filtering over 500 samples
• Confirmed Q8.15 fixed-point arithmetic match with model
• Verified math accuracy for 1k, 5k, 10k Hz coefficients
• sample_done counter exactly matched sample inputs
SPI Interface (tb_spi_master_full.v) Result: 71 / 71 Passed ✅
• Verified boot sequence (configured 4 registers via SPI)
• Confirmed DRDY synchronizer operations
• Verified CPOL=1, CPHA=1 protocol constraints
• Confirmed proper execution of 8 burst-read transactions
Regression Summary: Verification confirms Option 3 behaves exactly as designed. The Axis Sequencer rotates axes every 171 samples, and the Fault Flagger reliably detects and asserts a sticky interrupt at 6.4 ms per axis (19.2 ms full cycle) with no false alarms.
Notes: We performed extensive regression testing. All 79 verification assertions passed successfully. The top-level testbench verified Case 1 for normal operation and Cases 2, 3, and 4 for X, Y, and Z fault detection, confirming that axis indices are reported correctly and the interrupt asserts.
The Goertzel Core testbench confirmed Q8.15 fixed-point mathematical precision, and the SPI Master testbench passed 71 checks, verifying that the 4-register boot configuration and data-ready burst handshakes execute without error. This gives us high confidence for tapeout.

## Slide 10
SPACE-GRADE MECHANICAL FAULT DETECTOR
Roadmap & Key Takeaways
Key Contributions
1️⃣ Direct Digital MEMS Interface: Eliminates radiation-vulnerable analog components. End-to-end digital processing enables simple physical hardening of the logic.
2️⃣ Pragmatic Optimization (Option 3): Fits within the 600×600 µm Chipathon boundary with zero area cost, while speeding up vibration anomaly detection by three times.
3️⃣ Comprehensive Radiation Hardening (RHBD): Protects critical FSMs and configurations using TMR and majority voting, combined with background scrubbing and guard rings.
4️⃣ Verified & Tapeout-Ready: 79/79 verification tests passed. All block boundaries, timing, and math precision checks succeeded.
Project Roadmap
📅 Q3 2026:
Tape-out via SSCS Chipathon Shuttle (GF180MCU process)
📅 Q4 2026:
Laboratory post-silicon testing and power/latency measurement
📅 Q1 2027:
Implement Option 1 (Parallel Cores) to eliminate sequential data loss
📅 Q2 2027:
Flight qualify for educational CubeSat missions (TRL 5/6); open-source RTL
Notes: In conclusion, our ASIC demonstrates direct digital sensor integration and a highly optimized, radiation-hardened architecture. Option 3 solved our area constraint while accelerating fault detection.
Our next steps are highly realistic: we will tape out on the SSCS Chipathon shuttle, conduct post-silicon laboratory verification to measure power and latency, and then develop the parallel-core architecture to prepare for flight qualification on an educational CubeSat. Thank you, and I welcome your questions.